Product Specification

2/2021

| Product | LCD Display |
| --- | --- |
| Mode | APT LCD 500S |
| Abbreviation | 500S |
| Client |  |
| Customer audit |  |
| Supplier | APT(Tianjin) Develop Co., Ltd. |
|  | 1001, Building 5 HuaDing, No.1 HuaKe 3 Road, Binhai hi-tech Industrial Development Zone, Tianjin, China |
| Tel | TEL:+86 22 83715556 FAX:+86 22 83719955 |
| Email | yzhao@aptdevelop.com |

- Product Name

  - LCD display

  - Model : APT LCD 500S

- Suppliers

  - APT (Tianjin) Develop Co., Ltd.

  - Email : yzhao@aptdevelop.com  apt@aptdevelop.com

- Electrical Parameters

  - 24V/36V/48V/52V/COn battery supply

  - Rated operating current : 40mA

  - Off leakage current < 1uA

  - Max output current to controller : 100mA

  - Operating temperature : -20～70℃, Storage temperature : -30～80℃

- Dimensions & Material

  - Product shell is ABS, transparent window is made with high strength Acrylic.

  - Dimensions : host/L79mm*W40mm*H18mm

- Features

  - Suitable for low temperature，Max -20℃.

  - Ergonomic external button design, easy to operate.

  - Speed display: AVG SPEED, MAX SPEED, SPEED (Real-time).

  - Kilometer / Mile : Can be set according to customers’ habits.

- Assist level: 3-level/5-level/9-level/UbE optional.

- Mileage indicator: Odometer/Trip distance/Riding time.

- Error code indicator.

- Software upgraded: Software can be upgraded through UART.

- LCD screen instructions

- Functional Description

  - Power On/Off

Press and hold Power button for 2 seconds can turn on/off the display. The Display can automatically shut down when there is no operate & ride for X minutes（X could be 0~15）.

  - Assist level operating

Short press UP/DOWN button can change the assist level. Top assist level is 9, 0 for neutral. Level quantities can be adjusted according to the customer requirements.

  - Speed & Mileage mode switch

Short press MODE button can change the speed and mileage mode, AVG SPEED→MAX SPEED→ TRIP→ODO→TIME.

*If there is no operation for 5 seconds, display will return Speed (Real-Time) display automatically.

  - Headlight/backlight On/Off

Press and hold UP button for 2 seconds can turn on/off the headlight.

*The motor does not work when the battery voltage is low, Display still can keep the headlight on for a while when E-bike is in riding.

  - Walking mode (6km)

Press and hold DOWN button for 2 seconds can get into walking mode, out of the mode when release the button.

* This feature needs to be supported by controller.

- Parameter setting

Press and hold MODE button for 2 seconds can get into/ exit setting menu, press UP/DOWN button to change the parameter setting, press MODE button can switch to next item.

* Display will automatically quit menu when there is no operation for 10 seconds.

* For safety reasons, display can’t get into MENU when riding.

* Display will quit MENU when start riding.

The order of parameters is as follow.

  - Data clean up(Cr): Press Up/Down button to change no/yes.

  - System (S7): Press Up/Down button to switch between Metric/Imperial.

  - Brightness (bl): Press Up/Down button to change the brightness of the backlight, 1 is darkness, 5 is brightness.

  - Auto off (OF): Press Up/Down button to change the auto power off time, from 0~15, the number represent time (minutes) to shut down, 0 means disable auto off function, default value is 5 minutes.

  - Wheel (Hd): Press Up/Down can change the wheel setting, optional wheel diameter is 6~34 inch.

  - Password (Pd): Press MODE button can get into the advance setting menu, default password is ‘1919’.

  - Speed limit (SL): Press Up/Down button will change speed limit, range 10km~100km.

  - Battery (b0): Press Up/Down button to switch between 24V/36V/48V/52V/COn, Con means controller transfer voltage value.

  - Assist levels (PS): This parameter can customize assist levels, options are UbE/3/5/9.UbE means user-defined assist levels setting.

- Error Code define

500S can show warning message,  icon shows on the screen, and show error code at the bottom of the screen, error code is from 01 E~0nE, and the definition see the table below.

| Error Code | Error description | Handle |
| --- | --- | --- |
| 0x04 | Throttle turn back fault | Check throttle and connection. |
| 0x05 | Throttle error | Check throttle and connection. |
| 0x06 | Under voltage protection | Charge the battery |
| 0x07 | Overvoltage protection | Charge the battery |
| 0x08 | Hall error | Check the hall connection |
| 0x09 | three-phase power error | Check three-phase power line connection |
| 0x10 | The controller is overheated | Stop using 10 minutes to restart |
| 0x11 | Motor overheating | Stop using 10 minutes to restart |
| 0x12 | Sensor error | Check the sensor connection |
| 0x13 | battery temperature abnormality | Stop using 10 minutes to restart |
| 0x14 | Motor temperature sensor is abnormal | Check the sensor |
| 0x15 | Controller temperature sensor failure | Check the sensor |
| 0x21 | Speed sensor fault | Check the sensor |
| 0x22 | BMS Communication Error | Check the cable connection |
| 0x23 | Headlight error | Check the cable connection |
| 0x24 | Headlight sensor error | Check the cable connection |
| 0x25 | Torque signal error | Contact the supplier |
| 0x26 | Torque sensor speed error | Contact the supplier |
| 0x30 | Communication Error | Check the cable connection |

- Assembly instructions

Please pay attention to the screw’s torque value, damaged caused by excessive torque is not within the scope of the warranty.

- Connector descriptions

- Red wire :    Anode(24V/36V/48V/52V)

- Blue wire :    Power cord to the controller

- Black wire :   GND

- Green wire :  RxD (controller -> display)

- Yellow wire :  TxD (display -> controller)

- Certification

CE / IP65 (water proof) / ROHS.

# Text boxes

UP

DOWN

MODE

POWER

Data clean up

Brightness

Auto off

Wheel

Password

Battery

Speed limit

System

Assist

M4*10