Radtel IP68 Full Band 108-620Mhz Amateur Radio User manual

2.  Keyboard Explanation

- [PTT ] : Push to Talk Button。

- [Key side 1]: Short Press :Turn on/off Commercial FM radio。Long Press :Alarm Function。

- [Key Side 2]: Squelch Function。

- [MENU ]:Menu Selecting and Setting, And Confirm Function。

- [UP\DOWN]: Select Item Function Key。

- [EXIT]: Exit Key

In the standby mode ，Long Press to Switch between the frequency /Channel Mode.

- [ *	]: In the Standby mode, Short Press to Switch A/B Channel

And Long Press to Frequency copy mode (pick up the frequency from other radios and make the communicate immediately)

- [ #	]:In the standby ,Long press to keyboard  Lock and Unlock

3. Menu (Function) Setting

1.Short Press“MENU” into Level 1 Menu Interface。

2.”UP/DOWN ”      to Select  “ Level 1 Menu ” ，then Short press “MENU” again into  Level 2 Menu Interface。

3.”UP/DOWN ”      to select  “Level 2 Menu ”，then Short press “MENU” again into  Level 3 Menu Interface。

4.”UP/DOWN”      to Modify  parameter ，Finally Short Press “MENU”to Confirm and keep，Short Press“EXIT”to Cancel and back(not keep)。

For Example:

CTCSS/DCS Setting：

1.Short press“MENU”into Level 1 Menu Interface。

2．”UP/DOWN”     to Select  “CTCSS/DCS” ，Short Press“MENU”into Level 2 Menu Interface。

3.  Short Press ”UP/DOWN”      to Select  “CTCSS/DCS”or“R-CTCSS/DCS”or“T-CTCSS/DCS” ，Then Short Press“MENU”into Level 3 Menu Interface。

4.Short Press“*” key to Switch between CTCSS /DCS MODE（OFF/QT/DQT）.

Short press ”UP/DOWN”   to Select the Code of CTCSS/DCS。

Short Press“#”Key to Switch to Positive and negative code of CTCSS/DCS

5.  Short Press“MENU”To Confirm and save，Press“EXIT”To Cancel and Not save。

4. Frequency copy mode (pick up the frequency from other radios and make the communicate immediately)

1．In the Standby，Short Press“*”Key，Enter into Frequency copy mode。

2．Press UP or DOWN key to select the Channels which you captured need to save

3．Make the other radio to transmit，The Display show “Finished”when captured the frequency，Press PTT to go  Communicate with the transmit radio

4.  When finished ，Then press“MENU”to Save，Press“EXIT”to Reset for test。

5. Menu Parts

1) Receiving and Transmitting Function

| Item | Menu | LCD Display | Setting Selection |
| --- | --- | --- | --- |
| １ | Working Mode | Work Mode | VFO：only frequency MEMORY: channel frequency CH: channel number only |
| ２ | Step Frequency | Step | 5K/6.25K/10K/12.5K/25K/50K/100K The frequency step |
| ３ | RX Output Power | Power | High/Low High: High power Low: Low power |
| ４ | Squelch Level | SQL | 0-9 The Squelch level |
| ５ | Bandwidth | Bandwidth | Wide/Narrow The wide band: 25khz Narrow band: 12.5khz |
| ６ | Time-out Timer | TOT | OFF/30S/60S/90S/120S/150S/180S/210S/240S 270S The time prevent transmition |
| ７ | Busy Channel Lockout | BCLO | OFF/ON |
| 8 | Scrambler | Scrambler | OFF/ON Voice encryption |

2) CTCSS/DCS Function

| Item | Menu | LCD Display | Setting Selection |
| --- | --- | --- | --- |
| １ | CTCSS/DCS | C-CTC/DCS | OFF/CTCSS/DCS Press * button to switch to DCS tone, press * again to be OFF |
| ２ | CTCSS/DCS RECEIVING | R-CTC/DCS | OFF/CTCSS/DCS The receive frequency sub tone, Press * button to switch to DCS tone, press * again to be OFF |
| ３ | CTCSS/DCS TRANSMITTING | T-CTC/DCS | OFF/CTCSS/DCS The transmit frequency sub tone, Press * button to switch to DCS tone, press * again to be OFF |
| 4 | Special DCS tone on/off | SPEC-DQT | ON/OFF The special DCS sub tone |
| 5 | Special DCS tone type | SPEC-TYPE | Special/Normal/off |

3) Channels Function

| Item | Menu | LCD display | Setting Selection |
| --- | --- | --- | --- |
| １ | Channel Storage | Stor Channel | 1-199 To store frequency into channels |
| ２ | Channels Delete | Del Channel | 1-199 To delete frequency in channels |

4) Menu setting

| Item | Menu | LCD Display | Setting Selection |
| --- | --- | --- | --- |
| １ | Backlight time Select | Back Light | OFF/ON/5S/10S/15S The backlight off timer |
| ２ | Voice Prompt on/off | Voice | OFF/ON Enable/disable the voice annuncation |
| ３ | Beep tone | Key Beep | OFF/ON Keypad tone enable/disable |
| ４ | Language Select | Language | English/Chinese |
| ５ | Keyboard Lock | Key Lock | OFF/ON Auto keypad lock on/off |
| ６ | Saving model | Batt. Saver | OFF/ON Battery save function |
| ７ | Offset | Offset | 0-70M Repeater offset frequency |
| 8 | Repeater shift | SFT_D | OFF/+/- Offset direction |
| ９ | Double Standby | Double Rx | OFF/ON |
| 10 | Priority Transmitting | TX.SL | Edit/Busy |
| 11 | Squelch Tail tone Elimination | STE | OFF/ON End of transmit tone |
| 12 | Roger | Roger | OFF/ON Roger tone |
| 13 | Warn Mode | Warn Mode | TONE/TX TONE |
| 14 | Auto Shut off | APWR-OFF | OFF/4H/8H/16H/24H The time to power off radio |
| 15 | Turn-on Display | Open Msg | LOGO/Voltage Display logo or voltage when power on |
| 16 | Channel Name | Channel Name | OFF/Off |

5) VOX Function

| 1 | VOX Gain | VOX Gain | OFF/1/2/3/4/5 To activate VOX function, set 1-5 |
| --- | --- | --- | --- |
| ２ | VOX Delay | VOX Delay | 0-3S The delay time for VOX |

6) FM radio Function

| Item | Menu | LCD Display | Setting Selection |
| --- | --- | --- | --- |
| １ | Work Mode | Work Mode | VFO/CH Show FM radio channel or frequency |
| ２ | FM Monitor | FM-R | OFF/ON |
| ３ | Channels Storage | Stor Channel | 1-25 Store FM RADIO channel |
| ４ | Channels Delete | Del Channel | 1-25 Delete FM radio channel |

7) NOAA weather channel (for USA only)

| CH1 | 162.550 |
| --- | --- |
| CH2 | 162.100 |
| CH3 | 162.475 |
| CH4 | 162.425 |
| CH5 | 162.450 |
| CH6 | 162.500 |
| CH7 | 162.525 |
| CH8 | 161.650 |
| CH9 | 161.775 |
| CH10 | 163.275 |

Made by Xiamen Radtel Electronics Co.,Ltd

www.radtels.com